ANSA as a pre-processor for
LS-OPT optimization applications

---
Summary
Problem definition
Optimization Run
Pre-processing capabilities

---
Problem definition
Creating Morphing Boxes to the FE - Model

---
Problem definition
Creating Morphing Parameters
Section B

---
Problem definition
Creating Morphing Parameters

---
Problem definition
Connecting Morphing Parameters with Design Variables
Easily access Design Variables through an ascii file
$ DESIGN VARIABLES
$-------------------------------------------------------------------------------
$ ID | DESIGN VARIABLE NAME | TYPE | CURRENT VALUE | MIN VALUE --> MAX VALUE |
$-------------------------------------------------------------------------------
1 Section_A REAL 0. -5. 5.
2 Section_B REAL 0. -5. 5.
3 Section_C REAL 0. -5. 5.
4 Width REAL 0. 0. 8.
ANSA Scripting Language

---
Problem definition
Connect ANSA and solver to LS - OPT

---
Problem definition
Parsing Design Variables with LS - OPT
$ DESIGN VARIABLES
$-------------------------------------------------------------------------------
$ ID | DESIGN VARIABLE NAME | TYPE | CURRENT VALUE | MIN VALUE --> MAX VALUE |
$-------------------------------------------------------------------------------
1 Section_A REAL <<Section_A>> -5. 5.
2 Section_B REAL <<Section_B>> -5. 5.
3 Section_C REAL <<Section_C>> -5. 5.
4 Width REAL <<Width>> 0. 8.

---
Problem definition
Define Responses, Objective Function and Constraints

---
Optimization Run
Modifying Design Variables
Design Variables
$ DESIGN VARIABLES
$------------------------------------------------------
$ ID | DESIGN VARIABLE NAME | TYPE
$------------------------------------------------------
1 Section_A REAL <<Section_A>> -5. 5.
2 Section_B REAL <<Section_B>> -5. 5.
3 Section_C REAL <<Section_C>> -5. 5.
4 Width REAL <<Width>> 0. 8.
ANSA
LS-DYNA
LS-OPT
LS-OPT
Responses
Objective Parameters

---
Optimization Run
Modify ANSA model according to design variables
Output LS-DYNA file and model report
Design Variables
ANSA
LS-DYNA
LS-OPT
LS-OPT
Responses
Objective Parameters
hook.key
model_report.txt

---
Optimization Run
Invoke solver
Design Variables
ANSA
LS-DYNA
LS-DYNA
LS-OPT
LS-OPT
Responses
Objective Parameters
hook.key
LS-DYNA
output files

---
Optimization Run
Extract responses using LS-OPT functionality
Design Variables
ANSA
LS-DYNA
LS-OPT
LS-OPT
Responses
Objective Parameters
LS-DYNA
output files
model_report.txt

---
Optimization Run
Calculate objective function and constraints
Design Variables
ANSA
LS-DYNA
LS-OPT
LS-OPT
Responses
Objective Parameters

---
Optimization Run
The optimization algorithm calculates new values for the design variables
Design Variables
The process is repeated until the optimal solution is found
ANSA
LS-DYNA
LS-OPT
LS-OPT
Responses
Objective Parameters
Optimal solution

---
Shape optimization
Modifying shape using Morphing Parameters
Opening holes for weight reduction
Applying re-meshing for element quality improvement
Objective: Minimizing Mass, Retaining stiffness
Depth1
Slope_right
Slope_left
Holes_diameter

---
Shape optimization
Initial shape
Optimal shape
Objective: Minimizing Mass, Retaining stiffness

---
Creating Features
Creating simple features like ribs and beads using Direct Morphing
Modifying feature dimensions with Morphing Parameters
Length
Width
Depth

---
Creating Features
Creating simple features like ribs and beads using Direct Morphing
Modifying feature dimensions with Morphing Parameters

---
Edge Fitting
Fitting FE-Model on different shapes using target curves.
Handling the shaping with Morphing Parameters.

---
Edge Fitting
Fitting FE-Model on different shapes using target curves.
Handling the shaping with Morphing Parameters.

---
ANSA Model Values
Any value of an ANSA card can be defined as a parameter
Such parameters can be :
Material Properties
Element Length in re-meshing process
Shell Thickness
Thickness

---
Spotweld Optimization
Spotweld optimization is possible through ANSA functionality
As Design Variables can be set Connection parameters:
Spotweld distance
Number of Spotwelds
Spotweld diameter
Spotweld Distance: 50mm
Spotweld Distance: 30mm
Spotweld Diameter: 6mm
Spotweld Diameter: 4mm

---
Spotweld Optimization
Spotweld optimization is possible through ANSA functionality
As Design Variables can be set Connection properties :
Connection properties and materials
Application of different types of spotwelds to the Connections
Type: RBE3-HEXA-RBE3
Type: NASTRAN CWELD

---
Batch Mesh and Optimization
The batch mesh parameters and quality criteria can be used as Design Variables in the optimization loop
Such Variables can be:
Element length
Treatment of holes and fillets

---
Composite Material Optimization
Using the ANSA Laminate Tool for composite optimization.
Changing fabric orientation
Changing layer thickness

---
METAPost for optimization
METAPost can provide a fast and easy way to extract constraints and objective parameters from solvers result files
Support of binary or ascii result files
Calculations to extract the desired results

---
Thank You
… for your attention